HPI wants to thank you for your confidence in its products.

Please read this manual carefully to ensure years of enjoyment of this specialised high end electronic device.

- Control the breaker points for a correct setting.

- Remove or disconnect the existing condenser / capacitor

- Connect the yellow-green cable to the frame / chassis / GND (pin 1)

- Disconnect the signal cable from the breaker point to the – side of the HT coil

Reconnect this cable to the Mesonix box (pin 4)

- Connect the black cable from the Mesonix box to the – side of the HT-coil (pin 2)

- Connect the red cable from the Mesonix box to the + side of the HT-coil (pin 3)

An indicator LED will flash when the mesonix is running

| PIN | COLOUR | FUNCTION | PIN | COLOUR | FUNCTION |
| --- | --- | --- | --- | --- | --- |
| 1 | Yellow-green | GND / frame / chassis | 3 | Red | Coil + / 6V / battery / ignition switch |
| 2 | Black | Coil - | 4 |  | Contact breaker |

# Text boxes

+

-